# Networking 101

Encapsulation of application data descending through the layers described in RFC 1122
Source: Wikipedia

An example MAC address: 00:20:91:01:33:70
(coincidentally, in the vendor range of “J125, NATIONAL SECURITY AGENCY”)
MAC vendor ranges are issued by the Institute of Electrical and Electronics Engineers.

IP address ranges are issued by the Internet Assigned Numbers Authority to Regional Internet Registries, who issue smaller chunks to their members. It’s a hierarchical distribution model:

IPv6 Prefix Assignment mechanism with IANA, RIRs, and ISPs. Source: Wikipedia

This hierarchical nature of IP range distribution makes it possible to aggregate routing information. If ISP A knows that ISP B is responsible for 192.0.2.X, then 192.0.2.15 must be reachable through their network. How do these ISPs obtain this routing information? They use the Border Gateway Protocol for that. But that’s for another time. This is networking 101, people!

IPv4 and IPv6 address notation. Source: Wikipedia

The most common Ethernet Frame format, type II. Source: Wikipedia

3.1. Internet Header Format

  A summary of the contents of the internet header follows:

    0 1 2 3
    0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   |Version| IHL |Type of Service| Total Length |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | Identification |Flags| Fragment Offset |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | Time to Live | Protocol | Header Checksum |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | Source Address |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | Destination Address |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | Options | Padding |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

        Example Internet Datagram Header

        Figure 4.

  Note that each tick mark represents one bit position.
Source: RFC 791 – Internet Protocol
3. IPv6 Header Format

   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   |Version| Traffic Class | Flow Label |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | Payload Length | Next Header | Hop Limit |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | |
   + +
   | |
   + Source Address +
   | |
   + +
   | |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
   | |
   + +
   | |
   + Destination Address +
   | |
   + +
   | |
   +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Source: RFC 8200 – Internet Protocol, Version 6 (IPv6) Specification